## Slide 1: De novo Identification of DNA Modifications Enabled by Genome-Guided Nanopore Signal Processing
Oxford Nanopore Technologies Knowledge Exchange
Wednesday, July 5th, 2017
Marcus Stoiber, PhD, LBNL Postdoc (soon-to-be Oxford Nanopore Technologies)

## Slide 2: nanoraw
Outline
What is (and isn’t) nanoraw?
How does it work?
Example nanoraw pipelines
Practical/computational considerations
Future directions and a wafer-thin intro to basecRAWller

## Slide 3: nanoraw
nanoraw is an open source python package (w/command line interface) for the resolution of raw nanopore signal with a genomic alignment
nanoraw does NOT improve sequence output of nanopore reads
nanoraw events perfectly match a genomic segment
This primarily enables:
Genome-browser style visualizations of raw nanopore data
De novo testing for shifts in signal (indicative of modified bases)
Enhanced training datasets

## Slide 4: nanoraw Relevant links
nanoraw available through the python package index (and bioconda; thanks internet!):
https://pypi.python.org/pypi/nanoraw/0.4.2
Code is hosted on github (this presentation is included in docs/):
https://github.com/marcus1487/nanoraw
And full documentation is hosted on readthedocs:
http://nanoraw.readthedocs.io/
Pre-print is available on bioRxiv (hopefully in print soon;):
http://biorxiv.org/content/early/2017/04/10/094672

## Slide 5: nanoraw genome_resquiggle
Nanopore pairwise genomic alignment overlaid with raw signal
* Visualization available from plot_correction subcommand

## Slide 6: nanoraw genome_resquiggle
Raw nanopore signal (x-axis: time; y-axis: normalized current)

## Slide 7: nanoraw genome_resquiggle
Error-prone base calls

## Slide 8: nanoraw genome_resquiggle
Genomic bases from obtained from alignment (graphmap or BWA)

## Slide 9: nanoraw genome_resquiggle
Mismatch (a.k.a. Correct segmentation, but wrong base call)

## Slide 10: nanoraw genome_resquiggle
Genomic insertion (a.k.a. Incorrectly added segment in read)

## Slide 11: nanoraw genome_resquiggle
Genomic deletion (a.k.a. Extra segment needed in read)

## Slide 12: nanoraw genome_resquiggle
Resolve mismatch (Trivial: assign genomic base to that segment)

## Slide 13: nanoraw genome_resquiggle
Resolve insertion step 1: Remove segments surrounding insertion

## Slide 14: nanoraw genome_resquiggle
Resolve insertion step 2: Identify new segment(s) (details later)

## Slide 15: nanoraw genome_resquiggle
Resolve deletion step 1: Identify region surrounding deleted base

## Slide 16: nanoraw genome_resquiggle
Resolve deletion step 2: Identify new segments (details later)

## Slide 17: nanoraw genome_resquiggle
Identify new segments: Calculate running difference between neighboring windows of 4 observations

## Slide 18: nanoraw genome_resquiggle
Select N maximal running differences as new segments

## Slide 19: nanoraw plot_multi_correction
With genome resolved signal reads are anchor by genomic position
Next step is to contract each base’s signal to fixed intervals

## Slide 20
Now we have comparable raw signal across all reads from a run
nanoraw plot_*

## Slide 21: nanoraw plot_*
Select genomic regions to plot via several criterion:
Maximum coverage (plot_max_coverage)
Genomic locations (plot_genome_location)
Centered on K-mer of interest (plot_motif_centered)
Require two sets of files:
Maximum difference in signal level (plot_max_difference)
Most significant difference in signal (plot_most_significant)

## Slide 22: nanoraw Statistical Testing
Detect modified DNA nucleotides genome-wide by comparison of amplified and native samples (Mann-Whitney U-Test)
Red: Amplified Black: Native

## Slide 23: nanoraw Statistical Testing
Testing-based Identification | Model-based Identification
No training data needed Identification of modified and un-modified bases in close proximity Any modification detectable | Exact chemical modification known Exact modification position known Only native DNA needed after training

## Slide 24
Output wiggle files for: Coverage, Signal, Signal SD, Length, P-values, Q-values, Difference
nanoraw write_wiggles

## Slide 25
All nanoraw analysis requires running genome_resquiggle
(more on this later)
Example pipelines:
  Modified base detection
  Visualize single run
  Visualize comparison of two runs
nanoraw Example Pipelines

## Slide 26
Modified base detection:
Run write_wiggles with 2 groups of fast5 directories and
specify –wiggle-types difference qval
Considerations:
Test statistic (u-test vs t-test; Fisher’s Method; Min. coverage)
Statistics filename
Stalled read filtering (more next slide)
nanoraw Example Pipelines
* Does not require installing R, rpy2 and ggplot2 (default pip install)
Notes: Also create fasta with most significant signal shifted regions without plotting support.

## Slide 27
Single Run Visualization:
Run plot_* with a single (set of) fast5 directory(ies)
Considerations:
Region Selection: Maximum coverage, genome location, motif centered
Over-plotting options: Raw (down-sampled), Boxplot, Quantile, Violin*
Number of bases and regions
Observations per base filter: Don’t include “stuck reads” when plotting. These can cause over-plotted from few reads.
nanoraw Example Pipelines
Notes: Based on percentiles of observations per base. Reads with 99th pctl <200 obs and max <5k obs would be "99:200 100:5000"

## Slide 28
Two Run Visualization:
Run plot_* with a two (sets of) fast5 directories
Considerations:
Region Selection: Most significant, largest difference
Q-value threshold (probably best to check this first)
Sequences file (fasta for the plotted regions)
nanoraw Example Pipelines

## Slide 29
nanoraw Practical Considerations
Re-squiggle Processing Architecture
Basecalled FAST5 Files
FAST5 Batch
FAST5 Batch
FAST5 Batch
FAST5 Batch
Re-squiggle Processes
…
Modified
FAST5 Files
Genome FASTA
Aligned Read
Aligned Read
Aligned Read
Aligned Read
…
Threaded Alignment Processes
…
Notes: Requires basecalling with events storage (note that minknow does not store events) albacore recommended for now

## Slide 30
nanoraw Practical Considerations
Re-squiggle Processing Architecture
Basecalled FAST5 Files
FAST5 Batch
FAST5 Batch
FAST5 Batch
FAST5 Batch
Genome FASTA
…
Threaded Alignment Processes
…
Choosing alignment parameters:
--align-batch-size: Each batch triggers a new system call to the mapper
--align-processes: Each processes must load the genome for each batch
--align-threads-per-process: Passed on to the mapper system call
Mapper: must provide either graphmap or bwa executable (argument should be runnable as provided)
Default behavior: 1 alignment process with 500 read batches; 1 re-squiggle process
Notes: Batch size to threads is very important. Bwa groups reads and threads finish independently, so large batches into many threads, but few processes can take a long time.

## Slide 31
nanoraw Practical Considerations
Re-squiggle Processing Architecture
Re-squiggle Processes
…
Modified
FAST5 Files
Aligned Read
Aligned Read
Aligned Read
Aligned Read
Re-squiggle Parameters:
--resquiggle-processes: Each process pulls one read off the queue at a time (relatively fast; esp. for long reads)
--cpts-limit (and –timeout): Filter reads that require nanoraw to re-segment large single portions of a read
--normalization-type: normalization parameters are stored back into FAST5 (median or pA recommended).
--corrected-group: This is the group added to the FAST5 file. Default value links to other nanoraw commands
  --overwrite: delete old corrected group
Notes: Don’t use raw_pA

## Slide 32
nanoraw Practical Considerations
nanoraw FAST5 format:
/Analyses/RawGenomeCorrected_000/
  nanoraw version and linked basecalling slot
  BaseCalled_template
    Normalization parameters (shift, scale, outlier threshold, norm type)
    Alignment
      Mapping position and alignment statistics (clipping, indels and (mis)matches)
      genome_alignment and read_alignment: when zipped together gives the pairwise alignment for a read
      read_segments: Read base start positions within raw signal file
    Events
      Read_start_rel_to_raw: needed when using read_segments to access raw signal
      Stripped down version of ONT events format (mean, stdev, start, length, base)
Notes: Genome sequence included in files.

## Slide 33
nanoraw Practical Considerations
Other considerations:
2D and 1D2: Don’t use 2D complement for modified base testing. 1D2 complement should be good (not tested)
--recursive convenience option added for new sub-directory structure
  --fast5-pattern for more complex FAST5 stored reads (quote *)
--statistics-filename: Written first time statistics are computed and then loaded every time after that. Huge speed up for region selection, wig, etc.
Make sure processes are killed after aborting a run before starting another
Other plotting functions: motif_with_stats, cluster_most_significant, correction plots, kmer signal distribution

## Slide 34
nanoraw Future Directions
Define signal reference from all reads
Identify stretches of reads with signal that aligns better off-by-one (OBO) base
Extend stretches to maximal OBO region
Add and remove a segment before and after OBO region to correctly adjust the OBO region
Iterate
nanoraw 2.0: Iterative segmentation refinement

## Slide 35: basecRAWller Streaming Basecalling Directly from Raw Signal

## Slide 36: basecRAWller Streaming Basecalling Directly from Raw Signal
basecRAWller is a python based command line application for the training and running neural network based basecalling algorithm
No fee source code license for non-commercial use at basecRAWller.lbl.gov
To call bases with default model:
> basecRAWller call --fast5-basedirs path/to/fast5s/ \
--out-filename basecRAWller_reads.fasta
> basecRAWller call --fast5-basedirs path/to/fast5s/ \
--out-filename basecRAWller_reads.fasta \
--raw-checkpoint-directory raw_checkpoints_dir/ \
--ft-checkpoint-directory fine_tune_checkpoints_dir
Call bases from another model (from community or trained):

## Slide 37: Thanks!
LBNL
      Ben Brown
      Len Pennacchio
      Rob Egan
      Juna Lee
      Susan Celniker
University of Birmingham
      Nick Loman
      Josh Quick
      Robert Neely
LBNL
      Ben Brown
NERSC
      Prabhat
nanoraw
basecRAWller